## Slide 1: Applications of Isotopes at BNL
Cathy S. Cutler, Strategic Advisor of the Isotope Research and Production Department, Brookhaven National Laboratory
Immediate Past President of the SNMMI

## Slide 2: What is radioactivity?
Unstable nucleus of an atom “decays”
  Emits energy/particles (α, β-, β+, γ) to become stable
Sometimes things are naturally radioactive
Sometimes scientist force things to become radioactive

## Slide 3: Radiopharmaceuticals
Radiopharmaceuticals - Drugs that contain radioactive atoms
Radiopharmaceuticals are used for imaging and therapy
Diagnostic radiopharmaceuticals have no pharmacological effect
  Examples:
    Heart disease (e.g., 99mTc, 18F, 82Rb)
    Cancer (e.g., 18F, 68Ga)
Therapeutic radiopharmaceuticals deliver radiation therapy directly to a lesion
  Examples:
    Seeds for prostate cancer therapy (192Ir)
    Targeted therapy (90Y, 131I, 223Ra,177 Lu)
More than 20 million nuclear medicine procedures are performed each year in the US, ~ 50% of the global market
Nuclear medicine is ~ $2 billion USD/year industry
The health benefits and economic impact are enormous

## Slide 4: Applications of Nuclear Medicine
PET
Imaging
SPECT
Detection of
cancer and its spread
Detection and monitoring of
cardiovascular diseases
Identification of
neurologic and psychiatric diseases
Imaging of normal and abnormal functions of
excretory organs
Identification of regional tissue damage due to
infection or trauma
Identification and quantification of
endocrine disorders
Slide: 4/19

## Slide 5: How are radioisotopes produced?
Reactors
Generators
Accelerators

## Slide 6: The Radioisotope Generator
A “generator” or cow is a practical, convenient method to transport and use (milk) very short lived radioisotopes without having to produce them at each site
  long lived “parent” radioisotope decays into a short lived “daughter” radioisotope and
  the parent and daughter must be chemically separable
This technique has been of utmost importance to nuclear medicine

## Slide 8: Technetium (Tc) – 99m Used as a Medical Tracer Most common radioisotope used in diagnosis, with over 40 million procedures worldwide per year
AEC*
Industry
Foundation
Development
Market
Walter Tucker and Powell Richards
Labeled Red Blood Cells
Used for blood pool imaging, including cardiac first pass and gated equilibrium imaging and for detection of sites of gastrointestinal bleeding
BNL
Inventors
Tc-99m Generator
Other medical applications include:
Bone scans
Functional brain imaging
Immunoscintigraphy
Pyrophosphate for heart damage
* DOE (Formerly AEC)

## Slide 9
Notes: Molecular imaging using nuclear techniques has become fairly standard and most of what is needed can be purchased off the shelf by most Universities, hospitals, companies and national labs and put into operation. However, once you start discussing therapy you no longer are able to purchase what you need off the shelf. The activities are much higher and it becomes necessary to have very specialized facilities and experience to produce and handle the activities required. Most of what is needed is specially designed and made for the given application.

## Slide 10: What Is Molecular Imaging?
of biological processes at the molecular and cellular levels in humans and other living systems
Visualization
Characterization
Measurement
Notes: Here is the definition of Molecular imaging. But what exactly does this mean?
Molecular imaging is the use of imaging technologies to assess biological activity in the body. It provides a way to see, define and determine the biology of diseases (such as cancer and Alzheimer’s disease) and improve patient care.

## Slide 11: Development of FDG at BNL
Basic Research
Application
Development
Labelling a sugar molecule (glucose) allows the accurate measurement of energy utilization.
18FDG
By labelling in a specific position (2 position) this prevents complete metabolism of the sugar.
Richard Lambrecht and Ron Finn made the isotope (Fluorine-18) on the 60” cyclotron, and Tatsuo Ido and C.N. Wan developed a synthesis of FDG under the direction of Joanna Fowler and Al Wolf.
Avg 1495 PET scans per scanner for a total in the world of about 8 million scans per year
Distribution of PET scanners in the world
Circa 1976
Glucose

## Slide 12: First Report of 18FDG Uptake in Tumors
Basic Research
Application
Development
Soon after the development of FDG, interest grew in the Medical Department about the use as an energy utilization marker in other applications
Prantika Som
In the late 70’s Prantika Som and Hal Atkins investigated the use of FDG for cancer diagnosis
Dr. Hal Atkins
In 1980 they published the results
The use for cancer gradually grew clinically
Most of the 8 million PET scans done each year are for cancer diagnosis or treatment assessment

## Slide 13: How are accelerator radiopharmaceuticals produced?
QA/QC

## Slide 14
Worldwide in the 10’s
130
70 MeV or below
1400
30 MeV or Below
Breakdown of Cyclotrons Worldwide and Energy

## Slide 15
Proton beam
Cooling water
Target basket
110 MeV
93 MeV
30 MeV (C-slot)
68 MeV
RbCl 1
RbCl 2
Brookhaven Linac Isotope Producer (BLIP)
BLIP schematics
BLIP target stack

## Slide 16: Theragnostics
Theragnostics
  one radioactive drug is used to identify (diagnostic), and a second radioactive drug is used to treat (therapeutic) cancerous tumors and/or metastases.
Treat what we see, see what we treat.
Dx
Tx

## Slide 17: Peptide Receptor Imaging

## Slide 18: “Remarkable response to Bi-213-DOTATOC observed in tumors resistance to previous therapy with Y-90/Lu-177-DOTATOC”
Abbreviated decay chain: 225Ac 221Fr 217At 213Bi
GEP-NET = Gastroenteropancreatic neuroendocrine tumors
Ref. Morgenstern et al. J. Nucl Med 2012; 53 (Supplement 1): 455.
Before
After
High publicity: Study awarded Society of Nuclear Medicine Image of the year in 2012
SNMMI press release June 11, 2012
Case I: Shrinkage of liver and bone metastases after i.a. therapy with 11 GBq 213Bi DOTA-TOC
Case II: Response of multiple liver lesions after i.a. therapy with 14 GBq 213Bi DOTA-TOC
Before
After
Ga-68 DOTA-TOC

## Slide 19: High Specific Activity 72As – theragnostic pair to 77As
Imaging Isotope 72As (T1/2= 26 h)
Positron energy comparison
No-carrier added As-72 can be obtained from 72Se/72As generator
Accelerator production of 72Se from natRbBr(p,x) at high energy and 75As(p,4n) at intermediate energy has been reported
We are interested in 75As(p,4n) production route for which excitation functions up to 45 MeV have been reported
Isotope | 89Zr (3.27 d) | 68Ga (67.7 m) | 124I (4.18 d) | 72As (26 h)
Mean Eβ+, keV | 396 (22.7%) | 829.5 (88.9%) | 870 (22.7%) | 1170 (87.8%)
(p,n)
(p,4n)

## Slide 20: Measurements of 75As(p,x) excitation functions above 45 MeV*
Irradiation conditions:
Target material: GaAs foil, d×h=2.5×0.00254 cm
Beam current: ~30 µA, focused beam
Irradiation time: 2 h
Incident energy: 117 MeV incident, lower points achieved by degradation with Al degraders
Aluminum foil used for beam monitoring
Work done by Dr. Anthony DeGraffenreid

## Slide 21: Excitation functions for Se-75 and Se-72 production from As

## Slide 22: Large scale production of 72Se at 105-103.5 MeV

## Slide 23: Chemical Processing

## Slide 24: 72Se/72As Generator
Anion exchange
AG1-X8 (200-400 mesh)
  5 mL BV
Load in 0.3 M NH4OH
Rinse H2O
Rinse dilute HCl
Collect each fraction to determine
percent loaded

## Slide 25: 72As-Monoclonal Antibodies
Trastuzumab (Herceptin)
  2mg/mL/rxn
Daratumumab
  1mg/mL/rxn
  control
Test against patient specific tumor models
To visually observe
  Drug sensitivity
  Uptake
  Effectiveness
M-Ligand
Linker
Biomolecule

## Slide 26: 72As-mAb Cell Studies
72As-trastuzumab is incubated with gastric cancer cell lines for a 24 hour period
Cells are separated from the media and analyzed for radioactivity
Gastric Cancer Cell Uptake
Cpm
18.5 times uptake in cells!!!
Completed at Stony Brook University

## Slide 27: 72As-Trasztuzumab in NCI-N87 gastric cancer xenografts

## Slide 28
1. Umbricht, C. A et al. 44Sc-PSMA-617 for radiotheragnostics in tandem with 177Lu-PSMA-617—preclinical investigations in comparison with 68Ga-PSMA-11 and 68Ga-PSMA-617. EJNMMI Research 2017
2. Chernysheva, M., et al. Accelerator Production of Scandium Radioisotopes: Sc-43, Sc-44, and Sc-47. Curr Radiopharm 2021
Elementally matched theranostic radionuclides
(Pseudo)Radiolanthanides theranostic radionuclides
Theranostic radiometals

## Slide 29: Production methods for 44Sc
Cyclotron
Generator
Generator allows for sites without a cyclotron to obtain high radionuclidic purity 44Sc
44Ti (t1/2=58.9 y) can lead to a long-lasting generator
44Ca(p,n)44gSc/44mSc
47Ti(p,α) 44gSc/44mSc
Becker, K.V., et al. Cyclotron production of 43Sc and 44gSc from enriched 42CaO, 43CaO, and 44CaO targets. Front Chem 2023
Cingoranelli, S.J., et al. Production and purification of 43Sc and 47Sc from enriched [46Ti]TiO2 and [50Ti]TiO2 targets. Sci Rep 2023
Schmidt, C., et al. Current State of 44Ti/44Sc Radionuclide Generator Systems and Separation Chemistry Curr Radiopharm 2024

## Slide 30: Preclinical applications
1 h LNCaP
4 h LNCaP
24 h LNCaP
48 h LNCaP
[43Sc]Sc-PSMA-617 PET Imaging
[47Sc]Sc-PSMA-617 SPECT Imaging
Manuscript in preparation for Molecular Pharmaceutics

## Slide 31: Images Obtained with PSMA Ligands
PC-3 PIP = PSMApos tumor, PC-3 flu = PSMAneg tumor; Ki = Kidney, Bl = bladder

## Slide 32
First-in-Man Using 44Sc-PSMA-617

## Slide 33
PET/CT whole body images at different time points post-injection using [44Sc]Sc-PSMA-617: (A) 30 min (B) 120 min (C) 19 h.1
44Sc was obtained from 44Ti/44Sc generator2
4 patients were administered with an average of 1.36 ± 0.25 mCi2
[44Sc]Sc-PSMA-617 was revealed more similar characteristics to [177Lu]Lu-PSMA-617 than the routinely used [68Ga]Ga-PSMA-113
Clinical applications of 44Sc
2nd cartridge
Whole-body PET scans presented as MIP of (A) Patient 1 and (B) Patient 2 at 4 hours after injection of 44Sc-DOTATOC1
44Sc was produced by the 44Ca(p,n)44Sc1
2 patients were administered with an average of 2.36 ± 0.23 mCi1
1. Singh, A.; et al. First-in-Human PET/CT Imaging of Metastatic Neuroendocrine Neoplasms with Cyclotron-Produced 44Sc-DOTATOC: A Proof-of-Concept Study. Canc Biother Radiopharm 2017
2. Khawar, A.; et al. [44Sc]Sc-PSMA-617 Biodistribution and Dosimetry in Patients With Metastatic Castration-Resistant Prostate Carcinoma. Clin Nucl Med 2018
3. Eppard, E.; et al. Clinical Translation and First In-Human Use of [(44)Sc]Sc-PSMA-617 for PET Imaging of Metastasized Castrate-Resistant Prostate Cancer. Theranostics 2017.
[44Sc]Sc-DOTATOC
[44Sc]Sc-PSMA-617

## Slide 34: Physicochemical characteristics of β-emitters and α-emitters
β-emitters
Intermediate LET radiation (0.50–2.30 MeV) ; long range in tissues (1–12 mm of tissue penetration).
β-particles range: target clusters of cells (from 10 to 1,000 cells)
α-emitters
High-LET radiation (60–230 keV/μm)
Short to intermediate path length (212Pb: 50–80 μm) in tissues
Path length: target several cells (2–10 cells)
High LET causes Irreversible damage of double stranded DNA
Slide courtesy of Dr. M. McDevitt, Memorial Sloan Kettering

## Slide 35
M. Makvandi et al (2018) Targeted Oncology 13: 189-203

## Slide 36
Actinium-225 (9.2 d) Demand
27 molecules labeled with 225Ac are presently under development, among which 13 have already reached human test level1
The first 225Ac-radiopharmaceutical has entered the clinical phase III stage and might reach the market by 2028
Patient doses, as informed by clinical trials, are estimated at 1.1-2.4 mCi per patient kg2
Considering pre-injection decay, ~80 Ci at end of bombardment would be sufficient to treat 100,000 patients each year
1Zimmermann, R., Is Actinium Really Happening? J Nucl Med, Aug 2023
2Jang, A., et al., Targeted Alpha-Particle Therapy: A Review of Current Trials, Int. J. Mol. Sci. 2023, 24(14), 11626.
3Pallares, R.M, Abergel, R.J., Development of radiopharmaceuticals for targeted alpha therapy: Where do we stand?, Front. Med. 2022, Vol.9
225Ac emits four α-particles down to stable 209Pb [3]
Overview of ongoing targeted alpha therapy clinical trials [3]

## Slide 37: Addressing the Supply Chain: Various 225Ac/229Th Production Routes
Facility | Nuclear Reaction
Reactor (thermal neutrons) | 226Ra(3n,g)229Ra 229Ac229Th (plus 228Ra target)
Accelerator (electrons) | 226Ra(g,n)225Ra225Ac
Accelerator (low energy particles) | 226Ra(p,2n)225Ac 226Ra(a,n) 229Th 226Ra(p,pn) 225Ra 232Th(p,x) 229Th
Accelerator (high energy particles) | 232Th(p,x)225Ac 232Th(p,x)225Ra225Ac
Accelerator (high energy neutrons) | 226Ra(n,2n) 225Ra
Hot Cell Facility (233U processing) | 229Th decay to 225Ac

## Slide 38: Target Challenge: develop thick Th targets to withstand high beam current to support clinical scale production
Initial targets were thin Th foils (0.127mm, 0.9g) encapsulated in Al. Used to support small scale production for chemistry development and for 225Ac cross section determinations.
Next larger diameter (0.38mm thick,13g )BNL targets to support new rastered beam at BLIP were sealed in inconel by electron beam welding.
Primary risk associated with Ci-Scale targets (~100g) is overheating. Capsule MP (1290°C) is lower than thorium MP (1755°C).
Thermal behavior at Th/capsule interface is key.
Thermal calculation for 165μA at 191 MeV incident energy assuming ideal thermal contact for a 3 mm thick target (105g) predicts low peak temperature but actual thermal contact conductance will be lower.
Targetry and Inventory

## Slide 39: Chemical recovery ~90%, >99% radiopurity, 225Ac/213Bi generator performance is equivalent to generators prepared from 229Th-derived 225Ac.
Preliminary Chemistry Flow Sheet

## Slide 40: Processing Facilities at BNL
Commissioned new AP hot cells for processing of Ac-225 to meet growing demand
AP hot cells in routine operations
MIRP put 112 mCi of Ac-225 into inventory by irradiation and processing all conducted here onsite (BLIP and AP hot cell) – great accomplishment!
DOE IP now has two processing sites: ORNL and BNL
Consist of three hot cells, two ready rooms, dedicated ventilation, acid scrubber system, clamshell for target introduction to reduce dose to operators.

## Slide 41: Pancreatic Ductal Adenocarcinoma (PDAC)
The most lethal common malignancy
  5 yr survival <10%
Onset of PDAC is typically asymptomatic
  Leads to 80-85% of patients presenting with metastasized disease or locally advanced disease
Surgery- chemo combo is the best chance for survival
PDAC detection at early stages increases survival chances
  There is a need for improved noninvasive detection methods
  The development of an immuno-PET strategy allows for noninvasive target specificity along with PET sensitivity
  225Ac radioimmunotherapy allows for treatment while limiting dose to healthy tissues

## Slide 42: Single platform for diagnosis and therapy
Therapeutics + Diagnostics
Theranostics
Targeting agent
(e.g. antibody)
Chelator
(e.g. MACROPA)
Therapeutic nuclide
(e.g. 225Ac)
Targeting agent
(e.g. antibody)
Chelator
(e.g. DFO)
Positron-emitting
nuclide
(e.g. 89Zr)
Imaging agent
Therapeutic agent
Notes: So what is a theranostic? A theranostic...
This approach combines the diagnostic and therapeutic agent into a single platform. For example, with your targeting antibody you can label it with a positron emitter, such as 89Zr, for diagnostic imaging and switch to a therapeutic radionuclide such as 225Ac for radioimmunotherapy.
The chelator will change with the nuclide change, however, since the antibody is the same you will maintain similar specificity for the target.

## Slide 43: Summary
The interest in therapeutic radionuclides is growing in leaps and bounds
The production is increasing making radionuclides more readily available
  DOE IP has ramped up its role in the supply with a goal of maximizing the domestic availability.
  Several commercial companies are pursuing production
A robust domestic supply of Ac-225 is being actively pursued in the U.S.
Alternative production approaches are being explored for all alpha-emitters.
These combined with new targeting molecules are resulting in advanced treatments for patients with limited to no options

## Slide 44: Questions ?